## Slide 1: SLAM for autonomous Race Cars
An Overview Christoph Winter Starkstrom Augsburg

## Slide 2: Outline
SLAM?
Theoretical Overview
Implementations (ROS)
Questions / Discussion

## Slide 3: SLAM?
Simultaneous Localization and Mapping
  Create a map of the environment
    Volumetric (Laserscanner, LiDAR)
    Feature-based
  Locate yourself relative to that map
    Fancy algorithms
  ???
  Profit

## Slide 4: Theoretical Overview
  Extended Kalman Filter SLAM
  Particle Filter SLAM
  Graph-based SLAM

## Slide 5: Terms
Scan matching: Matching a Laser Scan onto the map → Transform
ICP: Iterative Closest Points, a method for scan matching
Loop-closing:
  Perceiving already visited places (e.g. a previous part of the track)
  Detection of a loop-closing improves SLAM drastically
Data-association:
  Which sensed cone corresponds to which mapped cone?

## Slide 6: Extended Kalman Filter SLAM
Slides from Cyrill Stachniss
http://ais.informatik.uni-freiburg.de/teaching/ws18/mapping/

## Slide 7: Particle Filter SLAM
Slides from Cyrill Stachniss
http://ais.informatik.uni-freiburg.de/teaching/ws18/mapping/

## Slide 8: Graph-based SLAM
Slides from Cyrill Stachniss
http://ais.informatik.uni-freiburg.de/teaching/ws18/mapping/

## Slide 9: Implementations
GMappping (Grid Map, Particle Filter SLAM)
Mobile Robot Programming Toolkit (MRPT)
  Particle Filter SLAM (Grid Map or Point Map)
  EKF SLAM
  (Graph SLAM)
Many others:
  Karto SLAM (Graph-based)
  ORB-SLAM or LSD-SLAM (uses Camera as input)
  Hector SLAM
  …

## Slide 10: TF Setup
Proper TF Setup according to REP-0105
  map: Fixed Frame, no drift over time
  odom: Fixed Frame, can drift over time
  base_link: attached to the car
  map → odom: published by the SLAM package. Publish as fast as possible! (500-1000 Hz)
  map → base_link: yields position of the car
Transform detected cones immediately to the map frame!

## Slide 11: GMapping
Easy to integrate
Works best with LiDAR cone detections as input
  Hint: Convert (x,y) cone detection to (distance,angle) format to create the LaserScan message
Supports Multi-threading with a patch
  https://github.com/ros-perception/openslam_gmapping/pull/14

## Slide 12: MRPT
MRPT-1.5 branch for ROS Indigo
Difficult to integrate
Provides a metric ton of options
Awesome visualizations

## Slide 13: Others
Hector SLAM: Outputs unfiltered PoseWithCovariance, requires additional EKF
Camera techniques (ORB, LSD, …): Did not try, would love to hear some insights
Graph-based SLAM:
  Better suited for offline map generation
  Custom pose-graph generation could improve this approach for FSD

## Slide 14: Discussion

## Slide 15: See you at FSG* *hopefully